# SPECIFICATIONS - R/V Bounty Bay

Type:		Motor catamaran 			Bunks:		16 (12 PAX)

Length:	15.8 meters (60 ft) 			Beam:		6 meters (20 ft)

Engines:	Ford 120hp diesels (x2)		Range:		8,000 kms

Speed: 		6-8 knots 				Water:		1,200 litres

Fuel:		10,000 litres diesel			Displacement:	40 tonnes

Electronics:	Radar, Autopilot, GPS, SSB and VHF radios, Satellite phone

Safety Equipment:	2x 8 person Liferafts, 406 EPIRB, 121 EPIRB

Equipment:		Scuba tanks and compressor, Freezer, Fridge, Inverters

Inflatables:		2x 3.5m RIB inflatables and 1x 3.8m Achilles inflatable

Commercial Licence:	International Charter Vessel (Home port - Rarotonga)

Ground Tackle:	40 kg ploughshare anchor and 80 m x 12 mm galvanised chain